## Slide 1
MODULE 1.5a
SEPTIVOLT
The $1,000 Mistake:
Mastering Utility Bill Analysis & NEM 3.0
Utility Rate Structures · NEM 3.0 Economics · Battery ROI
"Most solar systems are sized wrong because reps never learned to read the bill."
SeptiVolt Solar Sales Accelerator™ | Energy Independence Education

## Slide 2
MODULE 1.5a
Reading the Bill: Tiered vs. Time-of-Use Rates
Tiered Rates: Baseline → Tier 2 → Tier 3 — usage volume triggers higher cost per kWh
Time-of-Use (TOU): Cost determined by WHEN power is used, not just how much (peak vs. off-peak)
Critical Field: 'Rate Schedule' or 'Rate Plan' — locate this first on every bill you analyze
Baseline Allowance: First X kWh at lowest rate — varies by utility and climate zone
Key Error Reps Make: Quoting 100% offset on raw kWh without splitting peak vs. off-peak usage
IMAGE
Split-screen diagram: left side shows a tiered rate staircase (Baseline/Tier 2/Tier 3 with $/kWh rising at each step); right side shows a 24-hour TOU clock graphic with peak hours (4-9pm) shaded orange and off-peak hours in blue. SeptiVolt branded.
⚡ PRO TIP: Point at the Rate Plan box and say: 'This 3-letter code tells us everything about how your utility charges you.'
SeptiVolt Solar Sales Accelerator™
Notes: Image: Side-by-side comparison of tiered vs. TOU rate structures with visual clarity.

## Slide 3
MODULE 1.5a
NEM 3.0: From Net Credit to Avoided Cost
NEM 2.0 (Legacy)
Excess solar credited at RETAIL rate (~28–32¢/kWh)
Net metering: true dollar-for-dollar offset
Systems sized for 100% offset actually achieved 100%
Minimal battery incentive — grid was a free 'battery'
Simple: produce more than you use, bank the credits
NEM 3.0 (Current Rule)
Excess solar credited at 'Avoided Cost' (~5–8¢/kWh) — 80% cut
Exporting power to grid now worth far less than buying it
100% production offset ≠ 100% bill offset anymore
Battery becomes the primary value driver — time-shifting is key
Design philosophy shift: maximize self-consumption, minimize export
⚡ PRO TIP: Tell the homeowner: 'NEM 3.0 changed the rules. Under the old system, the grid worked like a bank. Now, we design systems to use more of what you produce — which is why battery is part of every conversation.'
SeptiVolt Solar Sales Accelerator™

## Slide 4
MODULE 1.5a
Battery Storage Economics in NEM 3.0
5¢
Export Credit
What you earn sending excess solar to the grid (NEM 3.0)
45¢
Peak Buy Rate
What you pay utilities during evening peak hours (TOU E-TOU-C)
85%+
Self-Consumption
Achievable with battery vs. ~30% without — capturing full retail value
Battery ROI: Typical CA homeowner recovers battery cost in 3–5 years through avoided peak charges alone. Without battery, every excess kWh exported is a 40¢ arbitrage loss.
⚡ PRO TIP: Frame it this way: 'Battery isn't an upgrade — it's what makes solar financially complete in NEM 3.0. It turns a 5-cent asset into a 45-cent asset every single evening.'
SeptiVolt Solar Sales Accelerator™

## Slide 5
MODULE 1.5a
Non-Bypassable Charges: What Solar Can't Touch
Non-Bypassable Charges (NBCs) are mandatory fees applied to every kWh consumed — solar does not eliminate them
Common NBCs: DWR Bond Charge, Nuclear Decommissioning, Public Purpose Programs (CARE, FERA, wildfire funds)
Typical range: $0.02–0.05/kWh — appears small, but compounds to $200–400/year over system life
Critical Compliance Disclosure: 'Solar will dramatically reduce your bill but not to $0. These charges are utility-mandated and remain.'
Sales Impact: Setting this expectation pre-sale eliminates one of the top 3 causes of post-install complaints and cancellations
IMAGE
Screenshot-style graphic of a sample utility bill with NBC line items highlighted in red/orange circles. Annotation arrows pointing to: DWR Bond, Nuclear Decommissioning, PPPA Surcharge. Total NBC amount circled in bold at bottom.
⚡ PRO TIP: Say: 'Even with solar, you'll still receive a small utility bill — typically just the monthly connection fee plus these non-bypassable charges. Most clients see $8–15/month instead of $200+.'
SeptiVolt Solar Sales Accelerator™
Notes: Image: Annotated utility bill closeup showing NBC line items clearly labeled and highlighted.

## Slide 6
MODULE 1.5a
📋 Field Exercise: Find the Baseline
FIELD EXERCISE
1
Pull the sample utility bill from your Trainee Workbook (Page 12)
2
Identify the Rate Plan code — is this Tiered or TOU? Circle your answer
3
Locate the 'Baseline Allowance' — record the kWh amount and $/kWh rate
4
Add the 12-month usage summary — calculate annual kWh and average monthly kWh
5
Find and highlight all Non-Bypassable Charges — total the monthly NBC amount
6
Use the Bill Anatomy Script (Workbook p.13) to present your findings to your trainer in 90 seconds
⚡ PRO TIP: The rep who can read a bill in under 60 seconds, out loud, with confidence, earns the homeowner's trust before the proposal is even opened.
SeptiVolt Solar Sales Accelerator™