## Slide 1
MODULE 3.7a
SEPTIVOLT
The Hidden Discovery Process:
Technical Site Assessment Mastery
Panel Diagnostics · Attic & Basement Surveys · Conduit Strategy · Change Order Prevention
"The best solar reps gather 20 minutes of technical intel while the homeowner thinks they're just chatting."
SeptiVolt Solar Sales Accelerator™ | Energy Independence Education

## Slide 2
MODULE 3.7a
Electrical Panel Diagnostics: Amperage & Space
Step 1: Identify amperage — look at the main breaker (typically 100A, 150A, or 200A stamped on breaker)
Step 2: Count open slots — solar interconnect needs minimum 1 tandem (2-pole) breaker, battery may need 2
Step 3: Check bus bar rating — sometimes panel is labeled 200A but bus bar is only 150A (different spec)
Step 4: Photograph everything — panel label, main breaker, bus bar rating, all open/filled slots
Step 5: Log in your Site Assessment Form before leaving — memory fades; documentation protects you
IMAGE
Detailed electrical panel diagram with labeled callouts: Main Breaker (amperage), Bus Bar rating, Available slots (highlighted in green), Filled slots, and panel brand label. Educational engineering graphic style.
⚡ PRO TIP: Say: 'I need to photograph your panel for our engineering team — this is how we guarantee your system design is code-compliant before we finalize anything.' It's professional, not intrusive.
SeptiVolt Solar Sales Accelerator™
Notes: Image: Labeled panel assessment diagram for field reference.

## Slide 3
MODULE 3.7a
Attics & Basements: The Unsung Heroes of Site Survey
Attic Assessment
Rafter spacing (16" vs 24" OC affects racking cost)
Insulation type — blown-in may block conduit pathway
Ceiling height clearance for conduit/wiring runs
Existing roof penetrations (plumbing vents, HVAC) — inform panel layout
Evidence of prior leaks or repairs — roof integrity indicator
Basement / Garage Assessment
Location of main panel and sub-panels
Available conduit pathway from roof to panel
Battery mounting wall — must be non-combustible, level, code-compliant
Existing equipment (water heaters, HVAC) affecting install space
Pathway for EV charger rough-in if part of proposal
⚡ PRO TIP: Tell the homeowner: 'Quick look at your attic and garage takes about 5 minutes and saves weeks of engineering back-and-forth. The more I see today, the faster your install gets scheduled.'
SeptiVolt Solar Sales Accelerator™

## Slide 4
MODULE 3.7a
Conduit Run Strategy: The Aesthetic Sales Move
Exposed conduit is one of the top post-install complaints — address it proactively in the discovery
Conceal-first strategy: Always explore hidden conduit routes (attic/wall cavity) before defaulting to exterior exposed EMT
The 'Aesthetic Upgrade' Frame: 'Our team will plan the conduit route to minimize visibility — most homeowners don't even notice it once installed properly.'
Document the preferred route in your site notes — surprises during install create change orders
HOA Homes: Flag immediately — many HOAs require conduit to match roofline or be painted; engineering needs to know pre-permit
IMAGE
Before/After photo split: Left shows exposed conduit running visibly down stucco exterior (negative example). Right shows same home with concealed conduit via attic route — barely visible. Professional installation photography style.
⚡ PRO TIP: Walk the exterior of the home and say: 'I'm mapping the cleanest conduit route — this determines where the wiring runs from your roof to your panel. We want it to look as clean as possible.' This shows craftsmanship — not just salesmanship.
SeptiVolt Solar Sales Accelerator™
Notes: Image: Before/after conduit aesthetic comparison.

## Slide 5
MODULE 3.7a
Pre-empting Change Orders Through Discovery
A change order is a broken promise — every one costs you trust AND money (roofers, electricians, re-engineering)
Top Change Order Causes: MPU not flagged, roof condition not assessed, conduit path assumption, HOA requirements missed
Prevention Protocol: Use the Site Assessment Form (SAF) on every visit — no exceptions for 'easy' homes
The 'Expectation Buffer': Build a 5–10% scope contingency into your verbal communication early: 'Engineering may find something minor — we'll address it transparently if so.'
Disclose early = no surprise. Discover late = broken trust. Engineering change orders after contract signing are your #1 retention risk.
IMAGE
Visual checklist/funnel diagram: Discovery Inputs (roof, panel, attic, HOA, access) → Engineering Review → Clean Permit Package → Zero Change Order Install. Shows the quality pipeline that comes from thorough discovery.
⚡ PRO TIP: End every discovery with: 'Is there anything else about the home I should know — planned renovations, upcoming roof work, or electrical projects? Better to know now than discover it at install.'
SeptiVolt Solar Sales Accelerator™
Notes: Image: Change order prevention funnel showing how thorough discovery = clean installs.

## Slide 6
MODULE 3.7a
Incentive Mapping: SGIP, CARE & Local Rebates
Self-Generation Incentive Program (SGIP): California battery rebate — up to $1,000/kWh for qualifying storage installations
CARE/FERA Programs: Income-qualified utility discounts — if homeowner qualifies, recalculate their current bill against the discounted rate
Local Utility Rebates: Many municipal utilities (LADWP, SMUD, etc.) have separate rebate programs — verify by zip code
ITC Interaction: SGIP rebates reduce the basis for the ITC calculation — disclose this to avoid tax surprises
Documentation: All incentive claims require proper enrollment — sales rep responsibility ends at disclosure and application support
IMAGE
California map with utility territory overlays showing SGIP, CARE program coverage areas. Battery icon with dollar sign for SGIP, family icon for CARE. Color-coded by utility territory (PG&E, SCE, SDG&E).
⚡ PRO TIP: Always say: 'These programs change frequently — the numbers I'm sharing today are current, but I want you to verify with your tax advisor before relying on any credit amounts in your planning.'
SeptiVolt Solar Sales Accelerator™
Notes: Image: California utility territory incentive map.

## Slide 7
MODULE 3.7a
📋 Site Survey Prep Checklist
FIELD EXERCISE
1
Review homeowner's utility bill and 12-month usage before arriving on site
2
Check aerial satellite imagery (Aurora/Google) for shading, setbacks, and roof complexity
3
Prepare your Site Assessment Form — have it digital or printed, ready to fill on arrival
4
Photograph exterior: all roof faces, panel location, conduit entry points, HOA signage
5
Complete interior assessment: panel, attic, garage/basement — use your checklist every time
6
Debrief with homeowner using 'Next Steps' script before leaving — never leave without a clear timeline
⚡ PRO TIP: A rep who completes a Site Survey in under 30 minutes with a complete SAF is more valuable to engineering than one who spends an hour but brings back incomplete data.
SeptiVolt Solar Sales Accelerator™